## Slide 1: MicroControllers
Lecture 20 – IR Sensing
Spring 2020

## Slide 2: Today’s Lecture
IR Sensing
HW#9 Due Wednesday
Submit L20 Worksheet after class today
Assignment

## Slide 3: Infrared Sensing

## Slide 4: Infrared Sensing
Infrared (IR) sensing is used in many control applications
  TV, CD, DVD, audio/video remote control
  Remote control helicopters/cars
  Air-conditioning / Fans
Inexpensive and easy to use wireless communication technology
IR is invisible to the eye, although longer waves may be sensed as heat

## Slide 5: Wavelength
IR light is similar to visible light except it has a little longer wavelength
Range from 300GHz to 400THz

## Slide 6: IR in Environment
IR can be created from many sources
  Sun
  Light bulbs
  Circuit boards
  Candles
  Humans and animals
  Anything with heat

## Slide 7: AX-1838HS
In lab you will be working with the AX-1838HS IR Receiver Module.
  Miniature IR receiver
  Designed specifically for remote control applications
  Integrates sensor preamplifier and interface IC
  Outputs are CMOS and TTL compatible

## Slide 8: IR Modulation
Goal is to transfer a short sequence of bits
Receiver must be sensitive to transmitter but reject other sources of IR (ex. Sun or Lights)
Common modulation scheme is 38kHz pulse modulation, but carrier frequencies between 30kHz and 60kHz are often used

## Slide 9: 38kHz Pulse Modulation
Assume the remote transmitter in your lab is attempting to send the following byte : 10001010
Volts
Time

## Slide 10: 38kHz Pulse Modulation
To send a zero, transmitter remains off
To send a one, transmitter flashes at 38kHz
Volts
Time

## Slide 11: Transmitting and Receiving
SBProjects.com
Notes: Click picture for animation.

## Slide 12: Receiver
Must be chosen for correct modulation
  PD – Detection Diode receives original signal
  Preamp / Amp – Amplifies signal
  Limiter – Assists in obtaining a constant pulse level
  BPF – Tuned to carrier frequency (38kHz)
  Demodulator / Integrator / Comparator
    Work together to detect carrier frequency
    If frequency is present, comparator output is low

## Slide 13: Keys and Codes
#define UP 0xFF629D
#define DOWN 0xFFA857
#define LEFT 0xFF22DD
#define RIGHT 0xFFC23D
#define CENTER 0xFF02FD
#define ONE 0xFF6897
#define TWO 0xFF9867
#define THREE 0xFFB04F
Each button press results in a transmitted value
Print each key value to the serial monitor
Determine which code represents which key
Assign helpful names to each code value

## Slide 14: IR libraries
In lab we will be working with the IRremote library. The header file below must be included.
  #include <IRremote.h>
Assign input pin
Set up to use the library functionality

## Slide 15: Receive Data Using Library
To receive data call the decode function below
  Decodes the received IR message
  Returns 0 if no data ready, 1 if data ready
  Results of decoding are stored in the argument
    We will be using the results stored in IR_command_received.value

## Slide 16: Create Function to Decode Key Codes
Use the received key code to change the directionState of your state machine