## Slide 1: MicroControllers
Lecture 21 – Bluetooth
Spring 2020

## Slide 2: Today’s Lecture
Bluetooth Communication Introduction
Bluetooth Libraries
HW#9 Due Today
Assignment

## Slide 3: BlueTooth communication Intro

## Slide 4: What is Bluetooth?
Bluetooth is a wireless communication protocol
  Low power: 10 mA in standby, 50 mA while transmitting
  Low-cost: $5 per device
  Small: 9 mm2 single chips

## Slide 5: Limitations of Bluetooth
Bluetooth technology is prevalent, but limitations have prevented it from becoming the de-facto wireless technology
Short communication range
  Most Bluetooth devices are Class 2 which have a range of about 10 meters (30 feet)
  The more objects that are in between devices, the less range it will have
Slow transfer rate
  About 3 Mbits per second (compare to wifi which is 54 Mbps)

## Slide 6: Communication Model
Bluetooth is based on a master-peripheral model
  Up to seven active peripherals can be connected to form a local network (called a piconet)
  There may be other inactive or parked peripheral devices in the piconet. Up to 255 parked devices are allowed
Piconet
  Collection of devices connected in an ad hoc fashion
  Master-peripheral relationship is constant for the lifetime of the piconet
  Master determines hopping pattern (more to come), peripherals have to synchronize

## Slide 7: Piconet
P4
P3
P2
P1
P7
P6
P5

## Slide 8: Piconet
M = Master
S = Peripheral Device
SB = Standby
P = Parked

## Slide 9: Scatternet
Linking of multiple co-located piconets through the sharing of common master or peripheral devices
  Device can be peripheral in one piconet and master of another
Piconets
M = Master
S = Peripheral Device
SB = Standby
P = Parked

## Slide 10: Communication
Bluetooth uses a technique of time division duplex (TDD) to coordinate the access to the physical channel
  Time is divided into fixed length intervals (625 microseconds) called slots
  Each second is divided into 1,600 slots
  Master sets the ratio frequency and initiates a data communication

## Slide 11: Frequency Hopping
The master sets the frequency hopping sequence
  The 2.4 GHz band is divided into 79 channels with their frequencies 1 MHz apart
  In each slot both the master and the peripheral device switch to a different channel
  Hopping is done 1,600 times per second
  Technique is called FHSS (frequency hopping spread spectrum)
  The peripheral devices follow the hopping sequence set by the master using a special algorithm

## Slide 12: Frequency Hopping
The original signal is spread out among 79 1MHz bands
Packets may be 1, 3 or 5 slots long
Master transmit begins in even number slots
Peripheral transmit in odd number slots

## Slide 13: Frequency Hopping
Several Bluetooth nodes can share the same frequency band using different frequency-hopping sequences

## Slide 14: Slots
The master initiates communication
  Master transmits data to a peripheral device in even numbered slots
  Master receives data from peripheral device in odd numbered slots
  A peripheral device is only allowed to transmit data in a slot if the master has polled it or sent a data packet to it in a preceding slot
  The peripheral responds to the master by sending a data packet or a NULL packet if the peripheral has nothing to send

## Slide 15: Addresses
Each Bluetooth device has a unique fixed 48-bit address
  Assigned at the time the device is manufactured
  Two communicating devices need to know each other’s address
  Software programs can specify the address if programmers know it
  The address can also be discovered during the device discovery process
    The discovery process searches all devices nearby and identifies the one that matches a user-friendly name such as “Joe’s Phone”

## Slide 16: Transfer Protocols
Many transfer protocols are available between two Bluetooth devices
  A standardized set of protocols designed for a particular type of device is termed as a Bluetooth device profile
  Radio frequency communication (RFCOMM) profile emulates a serial cable.
    Used for devices such as PC, printers and modems
  Generic audio/video distribution profile (GAVDP) is used to stream video or audio data.
    Used for stereo headphones and laptops
  Audio/video remote control profile (AVRCP) provides a standard interface to control audio or video devices
    Used for headphones, speakers and TVs

## Slide 17: RFCOMM profile
Designed for serial communication
Supported by HC-05 (used in lab) for both master or peripheral mode

## Slide 18: RFCOMM profile
HC-05 is an inexpensive Bluetooth-UART module
  Has a UART interface for serial communication between the Bluetooth module and microprocessors
  Bluetooth interface for wireless communication between two Bluetooth modules
2.4 GHz radio

## Slide 19: Bluetooth Libraries

## Slide 20: HC-05
In lab you will be working with the HC-05 Bluetooth Module
  Implements Bluetooth wireless protocol
  2.4GHz ISM (industrial, scientific, medical)
  Short range, ~10 meters
  Capable of communicating with:
    Other HC05s
    Cell phones
    Most Bluetooth devices

## Slide 21: Download Application
To communicate with your HC05 you will need to download an app.
  Apps available for Android and iPhone
Once app is downloaded, you will need to pair with HC05 device before attempting to communicate.
App may ask for passcode, 1234

## Slide 22: Keys and Codes
Each button press results in a transmitted value
Print each key value to the serial monitor
Determine which code represents which key
Assign helpful names to each code value (ASCII)

## Slide 23: Software Serial library
In lab we will be working with the Software Serial library. The header file below must be included.
  #include <SoftwareSerial.h>
Assign transmit and receive pins
Create storage variable BT_value

## Slide 24: Setup to use Library
BT baud rate should be setup for 9600
To read if Bluetooth value is available:

## Slide 25: Create Function to Decode Key Codes
Use the received BT_value to change the directionState of your state machine